## Slide 1: CHAPTER 3 EQUILIBRIUM
CHAPTER OUTLINE
3/1 Introduction
SECTION A Equilibrium in Two Dimensions
3/2 System Isolation and the Free-Body Diagram
3/3 Equilibrium Conditions
SECTION B Equilibrium in Three Dimensions
3/4 Equilibrium Conditions
Bialobrzeski/Iaif/Redux Pictures

## Slide 2: Article 3/1 Introduction
Equilibrium Conditions (Eq. 3/1)
  Force Balance: ΣF = 0
  Moment Balance: ΣM = 0

## Slide 3: Article 3/2 System Isolation and the Free-Body Diagram
System Isolation
Free-Body Diagram
  The free-body diagram is the most important single step in the solution of problems in mechanics.

## Slide 4: Article 3/2 – Modeling the Action of Forces (1 of 4)

## Slide 5: Article 3/2 – Modeling the Action of Forces (2 of 4)

## Slide 6: Article 3/2 – Modeling the Action of Forces (3 of 4)

## Slide 7: Article 3/2 – Modeling the Action of Forces (4 of 4)

## Slide 8: Article 3/2 – Construction of Free-Body Diagrams
Step 1: Decide which system to isolate.
Step 2: Isolate the system by drawing a diagram which represents its complete external boundary.
Step 3: Identify all forces which act on the isolated system as applied by the removed contacting and attracting bodies, and represent them in their proper positions on the diagram of the isolated system.
Step 4: Show the choice of coordinate axes directly on the diagram.

## Slide 9: Article 3/2 – Examples of Free-Body Diagrams (1 of 2)

## Slide 10: Article 3/2 – Examples of Free-Body Diagrams (2 of 2)

## Slide 11: Examples

## Slide 12: Examples

## Slide 13: Article 3/3 Equilibrium Conditions
Scalar Format (Eq. 3/2)
  ΣFx = 0
  ΣFy = 0
  ΣMO = 0

## Slide 14: Article 3/3 – Categories of Equilibrium

## Slide 15: Article 3/3 – Two-Force Members
Definition
  Occurs when a body is in equilibrium under the action of two forces only.
Forces are…
  Equal
  Opposite
  Collinear
  Independent of Object Shape

## Slide 16: Article 3/3 – Three-Force Members
Definition
  Occurs when a body is in equilibrium under the action of three forces only.
Forces are Concurrent
Case of Parallel Forces

## Slide 17: Article 3/3 – Alternative Equilibrium Equations (1 of 2)
Case 1: Use of Two Moment Equations
  Case (a)
    Resultant Intersects Point A
  Case (b)
    Resultant Intersects Point A
    Resultant is Perpendicular to x-axis
  Equilibrium Conditions
    ΣFx = 0
    ΣMA = 0
    ΣMB = 0

## Slide 18: Article 3/3 – Alternative Equilibrium Equations (2 of 2)
Case 2: Use of Three Moment Equations
  Case (c)
    Resultant Intersects Point A
  Case (d)
    Resultant Intersects Point A
    Resultant Intersects Point B
  Equilibrium Conditions
    ΣMA = 0
    ΣMB = 0
    ΣMC = 0

## Slide 19: Article 3/3 – Constraints and Statical Determinacy
Important Terms
  Constraint
  Statically Determinant
  Statically Indeterminant
  Redundancy
  Degree of Statical Indeterminacy

## Slide 20: Article 3/3 – Illustration of Determinacy
Statically Determinant System
Statically Indeterminant System – Replace Roller A with a Pin

## Slide 21: Article 3/3 – Adequacy of Constraints (1 of 2)
Complete Fixity (Adequate Constraints)
Excessive Fixity (Redundant Constraints)

## Slide 22: Article 3/3 – Adequacy of Constraints (2 of 2)
Incomplete Fixity (Partial Constraints)
  Concurrent Reactions
Incomplete Fixity (Partial Constraints)
  Parallel Reactions

## Slide 23: Article 3/3 – Approach to Solving Problems
Identify clearly the quantities which are known and unknown.
Make an unambiguous choice of the body (or system) to be isolated and draw its complete free-body diagram.
Choose a convenient set of reference axes.
Identify and state the applicable force and moment equations which govern the equilibrium conditions of the problem.
Match the number of independent equations with the number of unknowns in the problem.
Carry out the solution and check the results.

## Slide 24: Article 3/3 – Sample Problem 3/1 (1 of 4)
Problem Statement
  Determine the magnitudes of the forces C and T, which, along with the other three forces shown, act on the bridge-truss joint.

## Slide 25: Article 3/3 – Sample Problem 3/1 (2 of 4)
Solution I (Scalar Algebra) with x-y axes

## Slide 26: Article 3/3 – Sample Problem 3/1 (3 of 4)
Solution II (Scalar Algebra) with x′-y′ axes

## Slide 27: Article 3/3 – Sample Problem 3/1 (4 of 4)
Solution III (Vector Algebra) with x-y axes

## Slide 28: Article 3/3 – Sample Problem 3/1 (4 of 4)
Solution IV (Geometric)

## Slide 29: Article 3/3 – Sample Problem 3/2 (1 of 3)
Problem Statement
  Calculate the tension T in the cable which supports the 1000-lb load with the pulley arrangement shown. Each pulley is free to rotate about its b earing, and the weights of all parts are small compared with the load. Find the magnitude of the total force on the bearing of pulley C.

## Slide 30: Article 3/3 – Sample Problem 3/2 (2 of 3)
Free-Body Diagrams
Equilibrium Conditions for Pulleys A and B

## Slide 31: Article 3/3 – Sample Problem 3/2 (3 of 3)
Equilibrium Conditions for Pulley C

## Slide 32: Article 3/3 – Sample Problem 3/3 (1 of 2)
Problem Statement
  The uniform 100-kg I-beam is supported initially by its end rollers on the horizontal surface at A and B. By means of the cable at C, it is desired to elevate end B to a position 3 m above end A. Determine the required tension P, the reaction at A, and the angle 𝜃 made by the beam with the horizontal in the elevated position.

## Slide 33: Article 3/3 – Sample Problem 3/3 (2 of 2)
Free-Body Diagram
Equilibrium Conditions

## Slide 34: Article 3/3 – Sample Problem 3/4 (1 of 3)
Problem Statement
  Determine the magnitude T of the tension in the supporting cable and the magnitude of the force on the pin at A for the jib crane shown. The beam AB is a standard 0.5-m I-beam with a mass of 95 kg per meter of length.

## Slide 35: Article 3/3 – Sample Problem 3/4 (2 of 3)
Free-Body Diagram
Equilibrium Conditions

## Slide 36: Article 3/3 – Sample Problem 3/4 (3 of 3)
Graphical Solution

## Slide 37: Article 3/4 Equilibrium Conditions (3D)
Equilibrium Conditions (Eq. 3/1 extended)
  Force Balance: ΣF = 0
    ΣFx = 0
    ΣFy = 0
    ΣFz = 0
  Moment Balance: ΣM = 0
    ΣMx = 0
    ΣMy = 0
    ΣMz = 0
  The moment sum is taken about any convenient reference point.

## Slide 38: Article 3/4 – Modeling the Action of Forces (1 of 2)

## Slide 39: Article 3/4 – Modeling the Action of Forces (1 of 2)

## Slide 40: Article 3/4 – Categories of Equilibrium

## Slide 41: Article 3/4 – Constraints and Statical Determinacy
Complete Fixity (Adequate Constraints)
Excessive Fixity (Redundant Constraints)

## Slide 42: Article 3/4 – Constraints and Statical Determinacy
Incomplete Fixity (Partial Constraints)
  No Moment Resistance about Line AE
Incomplete Fixity (Partial Constraints)
  No Force Resistance along y-Axis

## Slide 43: Article 3/4 – Sample Problem 3/5 (1 of 4)
Problem Statement
  The uniform 7-m steel shaft has a mass of 200 kg and is supported by a ball-and-socket joint at A in the horizontal floor. The ball end B rests against the smooth vertical walls as shown. Compute the forces exerted by the walls and the floor on the ends of the shaft.
x
y
z
Ay
Az
Ax
Bx
By
W=200*9.81
W
5 unknowns
6 eq. Equations
Statically determinate problem
Fx=Ax+Bx=0
Fy=0=By+Ay=0
Fz=0=-W+Az=0 Az=W
rAB
rAw
MA=rABxB+rAWxW
rAB=(xB-xA)i+(yB-yA)j+(zB-zA)k
rAB=(0-2)i+(0-6)j+(3-0)k
Z=3m

## Slide 44: Article 3/4 – Sample Problem 3/5 (2 of 4)
Free-Body Diagram
Equilibrium Conditions – Moment Balance
-3By i+(-3Bx)(-j)+(-2By+6Bx)k
+3*1962 i+1*1962(-j)+0k
+ - +

## Slide 45: Article 3/4 – Sample Problem 3/5 (3 of 4)
Equilibrium Conditions – Force Balance
y
z

## Slide 46: Article 3/4 – Sample Problem 3/5 (4 of 4)
Equilibrium Conditions

## Slide 47: Article 3/4 – Sample Problem 3/6 (1 of 2)
Problem Statement
  A 200-N force is applied to the handle of the hoist in the direction shown. The bearing A supports the thrust (force in the direction of the shaft axis), while bearing B supports only radial load (load normal to the shaft axis). Determine the mass m which can be supported and the total radial force exerted on the shaft by each bearing. Assume neither bearing to be capable of supporting a moment about a line normal to the shaft axis.
W=mg
Ay
Az
Ax
Bx
Bz
200xsin60

## Slide 48: Article 3/4 – Sample Problem 3/6 (2 of 2)
Free-Body Diagram (Orthographic Projections)
Equilibrium Conditions

## Slide 49: Article 3/4 – Sample Problem 3/7 (1 of 3)
Problem Statement
  The welded tubular frame is secured to the horizontal x-y plane by a ball-and-socket joint at A and receives support from the loose-fitting ring at B. Under the action of the 2-kN load, rotation about a line from A to B is prevented by the cable CD, and the frame is stable in the position shown. Neglect the weight of the frame compared with the applied load and determine the tension T in the cable, the reaction at the ring, and the reaction components at A.

## Slide 50: Article 3/4 – Sample Problem 3/7 (2 of 3)
Free-Body Diagram
Moment Sum about Line AB

## Slide 51: Article 3/4 – Sample Problem 3/7 (3 of 3)
Remaining Equilibrium Conditions