## Slide 1
FE 376
FOOD QUALITY CONTROL
FATS AND OILS

## Slide 2
What is fat and oil?
A class of esters which results from the reaction of acids and alcohols
Fats and Oils – Triglycerides
+
Fatty acids
H2O

## Slide 3
Quality evaluation of fats and oils
The physical Quality parameters for plant oils:
Refractive index
Specific gravity
Color
Melting point
The chemical Quality parameters for plant oils:
Acid value
Peroxide value
Iodine value
Saponification value

## Slide 4
Experiment: Acid value

## Slide 5: WHAT IS THE AIM OF THE EXPERIMENT?
To determine acid value in an oil (or in the oil of a food product)

## Slide 6: PRINCIPLE?
ACID BASE TITRATION
Definition: the weight in milligrams of potassium hydroxide required to neutralize one gram of oil.
measurement of rancidity as free fatty acids are usually formed during decomposition of oil glycerides.

## Slide 7: Chemicals and Materials
Apparatus
Analytical balance
Erlenmeyer flask
Graduated cylinder
Balloon joje
Burette

## Slide 8
Ethyl alcohol- diethyl ether solution: 1:1 v/v mixture of ethanol and diethyl ether neutralized to phenolphthalein
Reagents
0.1 or 0.5 N Potassium hydroxide solution (standardized) : The solution should be colorless or straw yellow
Phenolphthalein indicator solution: Dissolve one gram of phenolpthalein in 100 ml of ethyl alcohol (95%)

## Slide 9: Procedure
2. Add 50 to 150 ml of a mixture of ethanol and diethyl ether (1:1 v/v) to dissolve the oil
4. Titrate, while shaking, with the 0.1 N KOH solution until the color of the indicator changes.
3. Add about one ml of phenolphthalein indicator solution
1. Weigh 5 to 10 g of oil into a 250 ml Erlenmeyer flask.
5. Steps above are repeated with a blank sample which does not contain any oil sample

## Slide 10: DATA TO RECORD
1
Weight of oil sample (g)
2
Volume of consumed potassium hydroxide solution (ml)
0.1 N KOH solution used for blank sample (Blank) Vb(ml)
0.1 N KOH solution used for sample (with oil sample) Vs(ml)
Vs - Vb = Vt (ml)

## Slide 11: CALCULATION
Acid value (mg KOH/g oil) =
Weight of oil sample (g)
Titre value (Vt)
x Normality of KOH
x 56.1

## Slide 12
Experiment: Peroxide value

## Slide 13: WHAT IS THE AIM OF THE EXPERIMENT?
To determine peroxide value in an oil (or in the oil of a food product)

## Slide 14: PRINCIPLE?
Peroxide value
The most widely used indicator of fat oxidation
measurement of the lipid peroxides and hydroperoxides formed during the initial stage of the oxidation.
The peroxide value is determined by measuring the amount of iodine which is formed by the reaction of peroxides with iodide ion.

## Slide 15: Chemicals and Materials
Apparatus
Analytical balance
Erlenmeyer flask
Graduated cylinder
Burette

## Slide 16
Saturated potassium iodade: Saturated solution of potassium iodide in distilled water is prepared. The solution must remain saturated
Reagents
0,1 or 0,01 N sodium thiosulfate (standardized) : The solution has to be kept well sealed and in the dark
Starch indicator solution : Dissolve one gram of starch in 100 ml of distilled water
Chloroform
Acetic acid

## Slide 17: Procedure
2. Add 10 ml of chloroform and 15 ml of acetic acid
4. Place the erlenmayer flask in a dark place for 5-10 min
3. Add about one ml of saturated potassium iodade solution
1. Weigh 5 g of oil into a 250 ml erlenmeyer flask.
Steps above are repeated with a blank sample which does not contain any oil sample
5. Add 75 ml of distillated water and 1 ml of starch solution (black-blue color)
6. Titrate, while shaking, with the 0.1 N sodium thiosulfate until solution turns from the dark blue into colorless.

## Slide 18: DATA TO RECORD
1
Weight of oil sample (g)
2
Volume of consumed sodium thiosulfate solution (ml)
0.1 N Na2S2O3 solution used for blank sample (Blank) Vb(ml)
0.1 N Na2S2O3 solution used for sample (with oil sample) Vs(ml)
Vs - Vb = Vt (ml)

## Slide 19: CALCULATION
Formula:
Peroxide value (meq/kg oil) =
Weight of oil sample (g)
Titre value (Vt)
x Normality of Na2S2O3
x 1000

## Slide 20
Experimet: Saponification value

## Slide 21: WHAT IS THE AIM OF THE EXPERIMENT?
To determine saponification value in an oil (or in the oil of a food product)

## Slide 22: PRINCIPLE?
Definition: weight of KOHin mg required to saponify 1 g of the oil or fat
Saponification - Hydrolysis of ester (triglycerides) under alkaline condition.

## Slide 23
Saponification Value
Tricaprylin (MW= 450)
Tristearin (MW= 890)
1Gram of Oils A and B
B
A

## Slide 24
Saponification Value
A
B
; Large molecular triglycerides
; Small molecular triglycerides

## Slide 25
Sample A has large molecular weight triglyceride (e.g. MW.890).
Sample B has small molecular weight triglyceride(e.g. MW.450).
In one gram of sample, number of triglyceride in B is about two times
more than number of triglyceride in A.
Less mg of KOH is needed to saponify sample A than sample B.
Therefore, saponification value of A is about half of that of sample B

## Slide 26: Chemicals and Materials
Apparatus
Analytical balance
Erlenmeyer flask
Graduated cylinder
Burette
condenser
water bath

## Slide 27
0.5 N HCl: Dilute 43.01 mL of 36.5-38% HCl to 1 L with distilled water
Reagents
0.5 N alcoholic KOH solution : Dissolve 28.055 g KOH in 1 L of alcohol.
Phenolphthalein indicator (1%): Dissolve one gram of phenolpthalein in 100 ml of ethyl alcohol (95%)

## Slide 28: Procedure
1. Weigh out accurately 2 g of oil ito a flask (A) and blank (B).
2. Add exactly 25 mL of 0.5 N alcoholic KOH solution.
3. Attach the reflux condenser and immerse the flask in boiling water for 60 min.
4. Swirl the flask frequently during the heating.
5. After refluxing, add 0.5 mL of 1% phenolphthalein and titrate with 0.5 N HCl.
6. Conduct blank determination.

## Slide 29: DATA TO RECORD
1
Weight of oil sample (g)
2
Volume of consumed HCl (ml)
0.5 N HCl solution used for blank sample (Blank) B(ml)
0.5 N HCl solution used for sample (with oil sample) A(ml)

## Slide 30: CALCULATION
Formula:
Weight of oil sample (g)
28.05
(B-A) x
Saponification value =

## Slide 31: Turkish Food Codex and TSE standards
Uçucu Madde (l05° C) | En çok % 0,2 (m/m)
Çözünmeyen Safsızlıklar | En çok % 0,05 (m/m)
Sabun Miktarı | Rafine yağlarda en çok % 0,005 (m/m) Soğuk preslenmiş ve natürel yağlarda bulunmamalı
Asit Sayısı | Rafine yağlarda en çok 0,6 mg KOH /g yağ Soğuk preslenmiş ve natürel yağlarda en çok 4,0 mg KOH/g yağ Natürel palm yağında en çok 10,0 mg KOH/g yağ
Peroksit Sayısı | Rafine yağlarda en çok l0 miliekivalen aktif oksijen / kg yağ Soğuk preslenmiş ve natürel yağlarda en çok l5 miliekivalen aktif oksijen / kg yağ
Ek-2 Diğer Kalite Kriterleri
The Turkish Food Codex (TFC) is a regulatory framework that includes standards, rules and regulations for food production, processing, consumption and trade in Türkiye. This codex was created to ensure food safety, protect the health of consumers and regulate trade in the food sector.
TURKISH FOOD CODEX NOTIFICATION ON OILS CALLED BY PLANT NAMES (NOTIFICATION NO: 2012/29)
Purpose
The purpose of this Notification is to determine the characteristics of the oils called by plant names within the scope of this Notification in order to ensure their production, preparation, processing, preservation, storage, transportation and marketing in a hygienic manner and in accordance with the technique.

## Slide 32: Turkish Food Codex and TSE standards
Bitkisel Yağlar | Bağıl Yoğunluk (Xo C/su 20o C) | Yoğunluk (g/mL) | Kırılma İndisi | Sabunlaşma Sayısı (mg KOH/g yağ) | İyot Değeri (Wijs) | Sabunlaşmayan Madde (g/kg)
Aspir Yağı | 0,922-0,927 X=20o C |  |  | 186-198 | 136-148 | ≤ 15
Aspir Yağı (yüksek oleik asitli) | 0,913-0,919 X=20o C 0,910-0,916 X=25o C | 0,912-0,914 20o C’de | 1,460-1,464 40o C’de 1,466-1,470 25o C’de | 186-194 | 80-100 | ≤ 10
Ayçiçek Yağı | 0,914-0,923 X=20o C |  | 1,461-1,471 40o C’de | 188-194 | 94-141 | ≤ 15
Ayçiçek Yağı (yüksek oleik asitli) | 0,909-0,915 X=25o C |  | 1,467-1,471 25o C’de | 182-194 | 78-90 | ≤ 15
Babassu Yağı | 0,914-0,917 X=25o C |  | 1,448-1,451 40o C’de | 245-256 | 10-18 | ≤ 12
Fındık Yağı | 0.898-0.915 X=20o C |  | 1,468-1,473 20o C’de | 188-198 | 81-95 | ≤ 15
Hindistancevizi Yağı | 0,908-0,921 X=40o C |  | 1,448-1,450 40o C’de | 248-265 | 6,3-10,6 | ≤ 15
Kanola/Düşük Erusik Asitli Kolza Yağı | 0,914-0,920 X=20o C |  | 1,465-1,467 40o C’de | 182-193 | 105-126 | ≤ 20
Mısır Yağı | 0,917-0,925 X=20o C |  | 1,465-1,468 40o C’de | 187-195 | 103-135 | ≤ 28
Palm Yağı | 0,891-0,899 X=50o C | 0,889-0,895 50o C’de | 1,454-1,456 50o C’de | 190-209 | 50,0-55,0 | ≤ 12
Palm Çekirdeği Yağı | 0,899-0,914 X=40o C |  | 1,448-1,452 40o C’de | 230-254 | 14,1-21,0 | ≤ 10
Palm Çekirdeği Olein | 0,906-0,909 X=40o C | 0,904-0,907 40o C’de | 1,451-1,453 40o C’de | 231-244 | 20-28 | < 15
Palm Çekirdeği Stearin | 0,902-0,908 X=40o C | 0,904-0,906 40o C’de | 1,449-1,451 40o C’de | 244-255 | 4-8,5 | <15
Palm Olein | 0,899-0,920 X=40o C | 0,896-0,898 40o C’de | 1,458-1,460 40o C’de | 194-202 | ≥ 56 | ≤ 13
Palm Stearin | 0,881-0,891 X=60o C | 0,881-0,885 60o C’de | 1,447-1,452 60o C’de | 193-205 | ≤ 48 | ≤ 9
Palm Süperolein | 0,900-0,925 X=40o C | 0,886-0,900 40o C’de | 1,459-1,460 40o C’de | 180-205 | ≥ 60 | <13
Pamuk Yağı | 0,918-0,926 X=20o C |  | 1,458-1,466 40o C’de | 189-198 | 100-123 | ≤ 15
Soya Yağı | 0,919-0,925 X=20o C |  | 1,466-1,470 40o C’de | 189-195 | 124-139 | ≤ 15
Susam Yağı | 0,915-0,924 X=20o C |  | 1,465-1,469 40o C’de | 186-195 | 104-120 | ≤ 20
Üzüm Çekirdeği Yağı | 0,920-0,926 X=20o C |  | 1,467-1,477 40o C’de | 188-194 | 128-150 | ≤ 20
Yer Fıstığı Yağı | 0,912-0,920 X=20o C |  | 1,460-1,465 40o C’de | 187-196 | 86-107 | ≤ 10
EK - 3 Bitkisel Yağların Fiziksel ve Kimyasal Özellikleri

## Slide 33: Turkish Food Codex and TSE standards